Session Summary Design Document

FitsViewer:
- draw_callback() paints from pixbuf1 into drawing area, then invokes self.refresh_circles_labels()
- load_file() will trigger reload_files() if something has changed and there's a valid file to load
- Holds two pixbufs, pixbuf0 and pixbuf1. Pixbuf0 holds the unscaled, full image, while pixbuf1 holds a scaled (zoomed) copy of pixbuf0
- Concept of a "slaved_view" which will have its center aligned with clicks in this FitsViewer (e.g., thumbs)
- Uses a separate RendererPane to control black/white settings
  - Concept of an "associated_renderer" allows one renderer to control multiple FitsViewers (e.g., thumbs)